## Slide 1: CAD HW4 - Modeling Mixed-Signal System and Simulating with AMS
Teaching Assistant: Tung Lin
Date: 12/13, 2022
Lab: ED-413

## Slide 2: Outline
Introduction to AMS
AMS Simulation Setup
  Analog Simulation with Verilog-A Model
  Mixed-Signal Behavioral Model Simulation
    Lab1: Analog Model Simulation with AMS
    Lab2: Mixed-Signal Model Simulation with AMS
    Lab3: 2-bit ADC with Verilog-AMS

## Slide 3: Outline
Introduction to AMS
AMS Simulation Setup
  Analog Simulation with Verilog-A Model
  Mixed-Signal Behavioral Model Simulation
    Lab1: Analog Model Simulation with AMS
    Lab2: Mixed-Signal Model Simulation with AMS
    Lab3: 2-bit ADC with Verilog-AMS

## Slide 4: What is AMS Designer
Top-down system-on-chip simulation for complex mixed-signal designs
A single executable simulator incorporating the fastest in digital and most flexible analog simulation capability
  Digital: NC-Sim
  Analog: Spectre
Simulation of complex designs incorporating any and all of the following:
  Verilog, VHDL
  Verilog-A, Verilog-AMS, VHDL-AMS
  Spectre
  SPICE
  Composer schematics

## Slide 5: What is AMS Designer(cont.)
NC-Sim
Digital Simulator
Spectre
Analog Simulator
AMS
Mixed-Signal Simulator
Waveform Display
Mixed Language Debugger
Verilog
Verilog-A

## Slide 6: Mixed-Signal Simulation with Model
The mixed-signal behavioral model simulation can verify:
  System behavior is correct or not?
  System requirement is met or not?
  System performance is satisfied or not?
Weaknesses:
  Only time domain information can be obtained directly
    All behavioral model should be converted into time domain
    Other characteristics might be calculated from time domain data

## Slide 7: Outline
Introduction to AMS
AMS Simulation Setup
  Analog Simulation with Verilog-A Model
  Mixed-Signal Behavioral Model Simulation
    Lab1: Analog Model Simulation with AMS
    Lab2: Mixed-Signal Model Simulation with AMS
    Lab3: 2-bit ADC with Verilog-AMS

## Slide 8: Environment Setting
NC-Verilog / Verilog-XL
  e.g > source /usr/cad/cadence/CIC/incisiv.cshrc
Spectre
  e.g > source /usr/cad/cadence/CIC/mmsim.cshrc
Composer / Virtuoso
  e.g > source /usr/cad/cadence/CIC/ic_06.17.709.cshrc

## Slide 9: Simulation Flow
Step 1. > virtuoso &
Step 2. Open library manager
Create library
Create cell view & symbol
  Verilog-A models
  Verilog models
  Schematic
  Config
Set ADE
Open library manager

## Slide 10: Simulation Flow
Create library
Create cell view & symbol
  Verilog-A models
  Verilog models
  Schematic
  Config
Set ADE

## Slide 11: Create Verilog-A Cells
Create library
Create cell view & symbol
  Verilog-A models
  Verilog models
  Schematic
  Config
Set ADE
Create a new cell view
Choose your library
Input the name on the Cell Name column
Choose the VerilogA type for Analog model
OK

## Slide 12: Designing with Verilog-A
Create library
Create cell view & symbol
  Verilog-A models
  Verilog models
  Schematic
  Config
Set ADE
Enter behavioral description

## Slide 13: Create Top Cell - Schematic
Create library
Create cell view & symbol
  Verilog-A models
  Verilog models
  Schematic
  Config
Set ADE
Input the name on the Cell Name column and choose the Schematic

## Slide 14: Create Top Cell - Schematic
Create library
Create cell view & symbol
  Verilog-A models
  Verilog models
  Schematic
  Config
Set ADE
Add Instance: Create→instance (i)
Add connection: Create → wire (w) gnd in the“basic” library
Add input/output: Create → pin (p)

## Slide 15: Simulation Environment
Open Analog Design Environment (ADE) in schematic editing window

## Slide 16
Through Setup -> Simulator/Directory/Host
Analog => spectre
Mixed-Signal => AMS

## Slide 17: Give input information(1/2)
If choose spectre as simulator, there only has stimuli
Input pin name in schematic

## Slide 18: Give input information(2/2)
Input high voltage and low voltage
Input pulse width and period
Pulse width =1/2 period
Check enable
1.
2.
3.
Voltage1:1.8V
Voltage2:0V
Period:20n
Pulse width:10n

## Slide 19: Choose Analysis Type
Choose tran analysis
Set the simulation time
and the accuracy flag
Check enable to simulation
6u

## Slide 20: Save Output Nodes
To Be Plotted:
  Select on line or node
  Press Esc to cancel

## Slide 21: Submit the Simulation
Execute the simulation job with Run
Tools → Results Brower
2.
1.

## Slide 22: Outline
Introduction to AMS
AMS Simulation Setup
  Analog Simulation with Verilog-A Model
  Mixed-Signal Behavioral Model Simulation
    Lab1: Analog Model Simulation with AMS
    Lab2: Mixed-Signal Model Simulation with AMS
    Lab3: 2-bit ADC with Verilog-AMS

## Slide 23: Create Verilog Cells
Create library
Create cell view & symbol
  Verilog-A models
  Verilog models
  Schematic
  Config
Set ADE
The cell name must be the same

## Slide 24: Design Hierarchy – AMS
Before creating the top schematic cell (add instance and connection), creating a config view for AMS simulation
Top Cell
<schematic>
Cell
instance
<Verilog-A>
Cell
instance
<Verilog-AMS>
Cell
instance
<schematic>
Cell
instance
<functional>
Cell
instance
<Verilog-A>

## Slide 25: Create Config View for Simulation
The mixed-signal simulation hierarchy is controlled by Hierarchy-Editor
  It must have to be defined in the config cell view.
Cell name is top schematic cell for simulation
Choose config type

## Slide 26: Set New Configuration
Select schematic view of top cell
Select AMS simulator in template
change to your library
Bottom view

## Slide 27: Configuration Setting
The hierarchy-editor will list all cells and views in the cell bindings
Must to save and recompute!

## Slide 28: Open Simulation Tool
Finish create config
  Click config at library manager to open simulation tool
  The simulation steps are the same as analog
    Except give input information
Confirm the title has “config”

## Slide 29: Digital Stimulus
Create a behavioral or functional view for the stimulus block
  The stimulus (Verilog) could be created to symbol view as the same procedure with digital cell

## Slide 30: Analog Stimulus
The analog stimulus can be added as circuit instance
Add Instance
Set voltage & frequency
Choose analogLib
& vpulse cell

## Slide 31
Setup
  Simulator choose AMS
Analysis
  Tran analysis
  Set simulation time and enable
Outputs
  Save all or select on design
Run
Waveform viewer

## Slide 32: Outline
Introduction to AMS
AMS Simulation Setup
  Analog Simulation with Verilog-A Model
  Mixed-Signal Behavioral Model Simulation
    Lab1: Analog Model Simulation with AMS
    Lab2: Mixed-Signal Model Simulation with AMS
    Lab3: 2-bit ADC with Verilog-AMS

## Slide 33: PLL Analog Model
All Verilog-A models are given
  PFD, CP, LF, VCO, sin2plus, divider
Import the Verilog-A models and setup ADE

## Slide 34: Additional Description
Connection
  Connect up (sigout_A) signal of PFD to siginc signal of CP
  Connect dn (sigout_B) signal of PFD to sigdec signal of CP
  Connect in signal of divider to sin2pulse
  Charge pump(CP)
    Connect vsrc to GND
VDD = 1.8V GND = 0V
Simulator: spectre
Input
  Fin=50M Hz : Set the ADE Stimuli
Simulation time ≧ 6μs
  Related to the lock time of PLL

## Slide 35: Results
Show the waveform of vctrl signal and schematic view
Top schematic cell
Observe the waveform of Vctrl
Open Results Brower

## Slide 36: Outline
Introduction to AMS
AMS Simulation Setup
  Analog Simulation with Verilog-A Model
  Mixed-Signal Behavioral Model Simulation
    Lab1: Analog Model Simulation with AMS
    Lab2: Mixed-Signal Model Simulation with AMS
    Lab3: 2-bit ADC with Verilog-AMS

## Slide 37: PLL Mixed-Signal Model
All models are given
  Analog model (Verilog-A): PFD, CP, LF, VCO, sin2plus
  Digital model (Verilog): divider
Import all models and create a testbench
  Testbench : generate rst signal for divider
Test bench
rst

## Slide 38: Additional Description
Connection
  Connect up (sigout_A) signal of PFD to siginc signal of CP
  Connect dn (sigout_B) signal of PFD to sigdec signal of CP
  Connect in signal of divider to sin2pulse
  Charge pump(CP)
    Connect vsrc to GND
VDD = 1.8V GND = 0V
Simulator: AMS
Input
  Fin=50M Hz, Adding voltage source instance
Simulation time ≧ 6μs
  Related to the lock time of PLL

## Slide 39: Results
Show the waveform of vctrl, output of the divider and schematic view
Top schematic cellview
Observe the waveform of Vctrl
Open Results Brower
Observe the output of divider.v

## Slide 40: Outline
Introduction to AMS
AMS Simulation Setup
  Analog Simulation with Verilog-A Model
  Mixed-Signal Behavioral Model Simulation
    Lab1: Analog Model Simulation with AMS
    Lab2: Mixed-Signal Model Simulation with AMS
    Lab3: 2-bit ADC with Verilog-AMS

## Slide 41: Description
Vref = 8V
7V
6V
5V
4V
3V
2V
1V
input = 3.5V
1
1
1
0
0
0
0
1
1
0

## Slide 42: Type : AMS
Support output reg

## Slide 43: Parameters of ADC Model
Input : sin wave
Amplitude : 4V, Frequency : 25M
Output : 2 bit output
R=1k, Vref=4V
Analysis Type : tran, 100n
Simulator: AMS
B1,B0 (bit) | Input (V)
00 | 0
01 | 1V
10 | 2V
11 | 3V

## Slide 44: Results
Hand in:
  The waveform of outputs of comparators, Encoder and Input
  Schematic cellview

## Slide 45: Hand in
Please upload a compressed file includes:
  Programming files (Verilog and Verilog-A files)
    Lab2: Stimuli (testbench.v)
    Lab3: Encoder file(.vams or .v), comparator file(.vams or .va)
  Mini report
    Three simulation waveforms
      Lab1: Analog simulation (Vctrl)
      Lab2: Mixed-signal simulation (Vctrl & output of the divider)
      Lab3: ADC(outputs of comparators, Encoder and Input )
    Three schematic cellviews
    What you have learned from this homework
    Questions and solutions
Deadline: 23:55, January 8, 2023